## Slide 1: A Realization of RFC XXXX Network Slices for 5G Networks Using Current IP/MPLS Technologies: Updates & Next Steps draft-ietf-teas-5g-ns-ip-mpls-01
IETF#118, Prague
November 2023
K. Szarkowicz (Juniper), R. Roberts (Juniper), J. Lucek (Juniper), M. Boucadair (Orange), L. M. Contreras (Telefonica)

## Slide 2: Summary of Issues & Resolution (1)
Assess which/whether some of the material in the "Network Slice Mapping" Section should be maintained in this draft or moved to the application I-D
  Sync with the authors of the application I-D
  The outcome is to keep the text in the realization I-D + Add NEW Scope text to both I-Ds to help decide if similar issues are raised in the future
  Proposed fix shared on the list (October 04, 2023): https://mailarchive.ietf.org/arch/msg/teas/4QifnnGAcnQcCTXRLSJtQ1SArLA/
  Removed the editor note used to flag the issue from draft-ietf-teas-5g-ns-ip-mpls-01

## Slide 3: Avoid Overlapping with teas-application I-D
This document focuses on the mapping between 5G Slices and underlying Transport Networks. Specifically, the document describes how RFC XXXX Network Slice Services can be derived in the context of a 3GPP Slice Service. To that aim, the document explores how and whether 3GPP Slice Service parameters are mapped to parameters that are exposed in IETF service data models (mainly, IETF Network Slice Service Model, Attachment Circuits'-as-a-Service (ACaaS), and bearers). It is out of scope of this document to elaborate on the realization of RFC XXXX Network Slices. These considerations are discussed in [I-D.ietf-teas-5g-ns-ip-mpls].
NEW Scope text added to draft-ietf-teas-5g-network-slice-application

## Slide 4: Avoid Overlapping with teas-application I-D
This document focuses on the technical realization of RFC XXXX Network Slices. The realization is typically triggered by Network Slice Service requests. How a Network Slice Service request is placed for realization, including how it is derived from a 5G Slice Service request, is out of scope. Network Slice Service mapping considerations (e.g., mapping between 3GPP to IETF service parameters) are discussed in [I-D.ietf-teas-5g-network-slice-application].
NEW Scope text added to draft-ietf-teas-5g-ns-ip-mpls

## Slide 5: Summary of Issues & Resolution (2)
Assess whether we need to maintain the "First 5G Slice vs Subsequent Slices" Section
  Updated the text to clarify why this is relevant to the realization
  Proposed fix shared on the list (October 06, 2023)
Clarify the use of inter-AS option B/C to model the AC between CE and PE
  Updated the text to insist on the specifics of this model compared to distributed and managed CE models
  Change to “service-aware CE”
  Proposed fix shared on the list (here) (October 06 , 2023)
Further discuss whether the TN slice in the customer site is covered or is out of the scope of Network Slice
  We agree that statement is ambiguous and, more importantly, does not bring much. What is important in that section is to describe the various orchestration domains.
  We deleted that statement
  Proposed fix already shared on the list (October 06, 2023)

## Slide 6: Other Changes
Added a NEW Section to cover « inter-AS Option C » considerations
And many other edits to enhance readability

## Slide 7: Next Steps
The authors think that the content is almost stable
  12 revisions so far
Proposal: Target WGLC by March 2024
  Request early directorate reviews right after IETF#118, especially
    rtg, opsdir, tsvart (QoS part), & intdir (addressing part)
  Seek external reviews on specific sections
    We already received some ACKs to review
    Contacted tsvwg for feedback
Comments are welcome
  Issues and PRs can be issued at https://github.com/boucadair/5g-slice-realization